## Slide 1
Spring term 2026
Lecture 3 Hardware design, implementation and testing
Embedded System Project (521423S-3006)
Jaakko Huikari
jaakko.huikari@oulu.fi
Marko Kauppinen
marko.kauppinen@oulu.fi

## Slide 2: Table of contents
Design phases
Achievements in the project so far
Summary of Phase 2
Electrical circuit simulator
Initial component selection
KiCad EDA (Electronic Design Automation)
KiCad schematics design
Ordering components
KiCad layout design
Fabrication outputs
Component placement on PCB
Hardware testing
Casing
Project budget and HW ownership
HW design support
Discussion

## Slide 3: Design phases
In practice:
Requirement specification, Technical specification, test plan, Schedule
Schematics, component ordering
Layout and manufacturing files, PCB ordering
Populating the board and electrical testing
Programming software and testing
Final demonstration and Final report

## Slide 4: Achievements in the project so far
Grouping up and topic selection has been completed
  Form a group of ~three
  Select a topic from the list
  Outline the main functionality of the device
  Topic selection documentation submitted
Phase 1 has been mainly completed
  Requirement and technical specifications mainly defined
  Component selection mainly fixed
  Test plan, project schedule etc.
  Phase 1 documentation
  ”Mainly” because minor or moderate changes to phase 1. are still possible during the next phase (Phase 2)

## Slide 5: Summary of Phase 2 (1)
Schematic design
  Components and their interconnections
  Outputs: netlist, BOM (Bill of Material)
Component ordering (BOM)
  Final component selection => shopping list => component ordering
Layout design (netlist)
  Actual physical stucture of PCB
  Locating of components
  Traces, vias, copper planes etc.
  Outputs: Manufacturing files (data suitable for PCB fabrication process)
PCB ordering
  Select a manufacturer
  Place an order, upload the manufacturing files

## Slide 6: Summary of Phase 2 (2)
Assembly i.e. populating the PCB
  PCB tests
  Soldering components
HW Testing
  Functions operate as designed
  Brace yourselves!
  Phase 2 might prove to be the most laborious one in the course.

## Slide 7: Summary of the main stages, tools and resources
Further understanding of the problem/ specifications / devices/ components
Component selection (initial)
Schematics design
Component selection (final) and ordering
Layout design
Manufacturing files for PCB
PCB ordering
Locating components on PCB
HW testing, debugging
Existing projects, datasheets, circuit simulators, course materials etc.
Providers, DigiKey, Mouser, etc., datasheets
KiCAD (recomm.), tutorials
Providers
KiCAD, tutorials
KiCAD, tutorials
JLCPCB (recomm.)
Manual work, lab resources?
Manual work, lab resources?
Course’s teaching staff
Stages
Tools and resources

## Slide 8: Electrical circuit simulator

## Slide 9
Circuit simulators that may help
First, try to keep your circuits as simple as possible, so that use of simulators could be avoided.
For very simple circuits, try Falstad’s online java circuit simulator
  https://www.falstad.com/circuit/
    Probably the simplest circuit simulator around.
    May be helpful for understanding and verifying simple circuits
    Op-amps, transistors, simple experimentation & learning…
    However, it does not model almost any of the non-idealities found in real circuits, so not to be blindly trusted.
If using Linear / Analog Devices controller ICs
  LTspice simulator includes almost all the LT / AD controllers, and a wide selection of related components for relatively easy testing
    https://www.analog.com/en/design-center/design-tools-and-calculators/ltspice-simulator.html
    Usually, simulation models are found on the product pages
There are also other simulators, most notable ones derived from the original Berkeley’s SPICE program
  Most are not beginner friendly, so choose carefully
  Perhaps one example, https://qucs.sourceforge.net/index.html

## Slide 10: Initial component selection

## Slide 11
Initial component selection
Suitable components
  Match with requirement and technical specifications
    Function, performance, technical constraints, costs etc.
  Solderability
  Availability of software support
How to find suitable components
Similar use case and project examples online
  Ideas about what components to use with certain applications
Datasheets, application & design notes from manufacturers
  Information about typical applications with schematics
Component suppliers (Digikey, Mouser, …)
  Component search engines in online stores

## Slide 12: KiCad EDA (Electronics Design Automation)

## Slide 13
KiCad, general introduction
KiCad is a free and open-source electronic design automation suite
Schematic capture, printed circuit board (PCB) layout, 3D rendering, and plotting/exporting data (manufacturing data e.g.)
Component libraries, thousands of symbols, footprints, and 3D models
  Custom-made symbols and footprints also possible
In this course we recommend to use the KiCad EDA
  https://www.kicad.org, software download
  https://docs.kicad.org/, instructions and guides
    Basic terminology, workflow, library settings, design examples etc.

## Slide 14
KiCad workflow on high level
Main design steps of the workflow at a high level
Create a new project
Schematic design (Schematic Editor)
  Symbolic representation of the circuit, components and their interconnections
  Footprint assignment
  Components as schematic symbols
PCB layout design (PCB Editor)
  Physical realization of the schematic
  Components as footprints
Fabrication outputs
  Data files for PCB manufacturing process (layers, traces, footprints, ground copper areas, vias, holes etc.)

## Slide 15
Need for self-learning to make progress
Some practical instructions and tips related to schematics and layout design practices are given
Far form all-inclusive
Independent study is absolutely needed
  As a team and as individuals
KiCad instructions, start here!
  https://docs.kicad.org/
  Cover whole design process
    Introduction, Getting started
    Schematics
    Layout
    Fabrication outputs etc.
  Instructions, guides, examples
More resources by searching online

## Slide 16: KiCad schematic design

## Slide 17
Schematic design workflow in a nutshell
Initial preparations
  Create a new project
  Electrical rules
  Setting up symbol library table
  Preferences (schematic editor)
  Schematic sheet setup
Add schematic symbols (i.e. schematic components)
Add connections between symbols (see datasheets)
Annotation and footprint assignment (take extra care in the latter!)
Electrical Rules Check (electrical errors, connection issues etc.)
Netlist (required for layout design)
Bill of Materials (components of the design => shopping list)

## Slide 18: Schematic design rules
Purpose is to ensure
  Connectivity
  Functionality
  Readability
  Manufacturability
Examples of design rule types
  Connectivity (pins, wires)
  Conflicts (duplicate reference designators)
  Miscellaneuous (missing annotation, similar labels)
  Pin conflicts (pin cofigurations, no connection)
Severity of violations (error, warning, ignore)
Start with default design rules settings

## Slide 19: A good schematic diagram
Purpose of reading schematics e.g.
  Symbolic presentation of circuit or system, (components, interconnections)
  Understanding how systems and components function
  Manufacturing and assembly of systems
  Testing, troubleshooting and repairing
Key features
  Clear, readable and unambiguous
  Logically structured
  Functional grouping of components
  Unique labels for each components
  Net labels instead of long messy wire bundles
  Standard symbols for components
  Comments for further understanding and information
Personnel reading schematics
  Other designers
  Technicians

## Slide 20: Practical schematic design, general
Start creating block diagrams
  High-level view of functional blocks
    Power supply, MCU, sensors, actuators etc.
Hierarchical schematic design
  Multiple hierarchical sheets according to different functions
    Sensors and interfaces on one sheet
    Power supply components on one sheet
    Main MCU and programmer pins on one sheet
  Enables blockwise assembly and testing later on
Comments
  Briefly explain less obvious subcircuits’ and components’ functionalities and details

## Slide 21: Practical schematic design, symbols
Adding symbols
  Components in KiCad libraries
  Custom-made symbols, symbol editor in KiCad
  More symbol libraries online, for example
    3dcontentcentral, Snapeda, Ultralibrarian, componentsearchengine, Octopart, Sparkfun, etc.
Annotation of components
  Unique reference designator to components
    “U1” (integrated circuit),”R2” (resistor) etc.
  Automatic symbol annotation option is recommended (KiCad)
Additional symbol info
  Add a field for component order number
    Name it, for example, “DigiKey”, “Mouser”, or similar
  Add a price field to each symbol
    Budget evaluation is necessary for your order list/ Bill-of-Materials (BOM).

## Slide 22: Practical schematic design, other
Net labels and data buses (i.e. connection without visible wire)
  Use net labels instead of long and messy wire bundle
  Use bus tool for grouped signals in data/ address buses
  Name signals clearly and logically
Footprint assignment
  Linking symbol (schematic) to footprint (layout)
  Make sure that selected components match with assigned footprints (SMD components, through-hole pin arrays)
    Details from datasheets e.g.
    Pin configuration
    Land pattern dimensions
    Package dimensions
  Multiple packages available
  Differences between packages may appear insignificant
  Be particularly careful here!

## Slide 23: Practical schematic design, other
Instant signaling/ alerts (LEDs, buzzers etc.)
  Important information about system at a glance
  System power and status (on/ off, measuring, data transmission, sleeping)
  Battery charge level etc.
Add test points
  Supply voltage nets (regulators, converters), sensor output nets, other important signal nets
Use no-connection flags for unconnected terminals
Tackle button bounce issue

## Slide 24: Practical schematic design, BOM
Bill of Materials
  List of component related values, reference designators and numbers
  Generate BOM once the schematic is finished
Can be generated with a Python script in KiCad
  See scripts from: \KiCad\bin\scripting\plugins
  Additional scrips can be found from the internet, or you can modify one to your needs
Alternative way to generate BOM
  “Edit Symbol fields” tool, paste to Excel for further processing

## Slide 25: Practical schematic design, electrical
IC related
  Use a pull-up or pull-down resistors if required (some IC pins e.g.)
  Use bypass capacitors for all ICs supply pins
  Never connect any signal driving IC pins directly to ground or power supply => IC may be destroyed in certain circumstances
  Unused IC pins, see datasheet (ground, Vdd, floating)
Voltage regulators and supply voltage designs
  Switching mode regulators have ripple voltage and cause EMI, which needs to be considered
Consider need for cooling in case design includes
  Linear regulators
  Motor driver circuits
  High-power RF transmitters
More on cooling requirements in datasheets

## Slide 26: Electrical Rules Check (ERC)
What is ERC
  Automated verification of electrical integrity of circuit before physical layout
    Connectivity
    Pin configurations
    Component annotation
    Power/ ground net integrity etc.
Run ERC often
  Prevent any schematic errors from passing to layout design
  Personal learning
  To avoid extensive and laborious changes at later phases

## Slide 27: Netlist
A text file including all components in schematic, their electrical connections and assigned footprints
Output of schematic editor
Starting point of layout design
Loaded to PCB editor after the schematic is completed
  Be absolutely sure that nothing important is left unconnected
  Run ERC during design (all errors are not critical from the point of view of the netlist, but less errors is better)
“Generate netlist” generates the netlist file in older KiCad
  Should be automatic in Kicad 6.x and later
  Load the netlist in PCB editor
Revision of schematics later on
  Update netlist
  Reload the updated netlist in the PCB editor with the latest changes
    In Kicad 6.x and later versions, use the “Update PCB with schematic changes button”

## Slide 28: Keeping notes and tips for further information
Keep notes during schematic design
  Traceability of design (steps, phases, development, details)
    What has been done, why and when?
    What has been changed, why and when?
  Personal learning (what has worked, what has not)
  Knowledge transfer
Online search tips e.g.
  “How to schematic design”
  “How to schematic footprint assignment”
  “Common mistakes to avoid in schematic design”
  Critical evaluation of sources

## Slide 29: Ordering components

## Slide 30
Final selection components and ordering
List of final components
Schematic is completed
  All the required components and their connections included
  With schematics done, the chance that something is left out of the order list is minimized
Permission to order components
Requirement and technical specifications are mainly complete
Schematic is about ready
Permission to order is given by the course staff
Important reminder!
Footprint assignment (schematic editor)
  Selected components has to match with assigned footprints

## Slide 31
Component suppliers
Examples of sites with very large selections (cheap individual ICs and other components, include also breakout boards and dev-kits, which may cost more than in other stores):
  Digikey (preference?)
  Mouser
  TME
  Farnell, etc.
Some more hobby & dev-kits oriented sites:
  Adafruit
  Sparkfun
  Pololu
  HobbyKing, etc.
If you order components through the university at the course’s expense, all the components must be included in one order. Only order from 1, or 2 places at most, otherwise, strong justification is required.
When ordering, be very careful about the delivery time. In many cases, for example, sources from China may claim much shorter delivery times than what they are in reality, so primarily look options from Europe and US area based companies / sellers, like the ones listed.
Verify availability of components (sufficient amount in stock, product status is still active)

## Slide 32: KiCAD layout design

## Slide 33: Layout design workflow in a nutshell
Initial preparations
  Design rules
  Layer stack-up definition
  Preferences (editor) etc.
Import design data from the schematic editor (netlist file)
Drawing a board outline
Placing footprints (components)
Routing tracks
Placing copper zones (ground and power supply connected)
Design Rule Checking (violations of manufacturing, electrical and physical constraints)
Fabrication outputs (necessary layers, file formats matching with manufacturer’s requirements)
Layout design can be started only after schematic design is completed and reviewed successfully by course staff

## Slide 34: PCB (Printed Circuit Board)
What is PCB
  Immediate electrical environment for electrical components and their interconnections
  Substrate/ base providing mechanical support and electrical connections
Typical structure of PCB
  Multitude of varying complex layered structures of dielectrics and conductors
  Typically made of fiberglass/ plastic and copper (e.g. FR-4, polyimide, Teflon, ceramic)
Electrical characteristics of PCB
  Complex structures with complex electrical interactions => complex electrical characteristics of its own
    => PCB is an electrical component in itself
  Unintentional electrical characteristics (resistance, inductance, capacitance)
    Known as parasitics
  PCB parasitics become part of circuits => might have adverse effects on performance
  Effects can be controlled to some extend by careful design of structures on PCB

## Slide 35: Professional layout design vs. practices on this course (disclaimer)
Professional layout design
  Complex electromagnetic phenomenona and interactions in and between systems
  Serious layout design and analysis requires professional design tools
  Serious PCB implementation requires iterative prototyping (trial and error method)
Post-layout simulation tools
  Extraction of parasitics emerging from actual physical geometry of designed structures
  Electrical model of PCB based on paracitics
  Analysis of PCB
    Signal and power integrity
    EMC/ EMI
    Thermal performance etc.
On this course instead
  Relatively simple and well-behaved circuits and systems
  No post-layout tools in KiCad (to my knowledge)
  Aiming to increase awareness, knowledge and understanding of good layout practices
  Practices applied to viable extend

## Slide 36: A good layout design
Purpose of PCB layout design
  Enable a functioning systems with sufficient performance (PCB as an electrical component)
  Manufacturable systems
  Realiable systems
    Electrical reliability
    Temperature management etc.
Potential conflict between the above
  PCB layout design is a compromise
Main variables in layout design
  Component placement (routing, signal integrity, thermal performance)
  Trace routing (power supply stability, signal integrity)
  Copper planes (power supply stability, signal integrity, thermal performance)

## Slide 37: PCB design rules, confines to design
Geometric constraints on design
  Minimum values: track width, clearance, via diameter etc.
Absolute limits are set by PCB fabricator’s physical fabrication limits
Global Design Rules, generally you should use
  Minimum track width: 0.25 mm, minimum clearance: 0.2 mm
  Minimum via drill diameter: 0.5 mm
  Minimum via/ through hole pad diameter: 1.5 * hole diameter
  More detailed design rule/ PCB related suggestions will be put available on the Moodle page
Netwise design rules, if needed
  Larger tracks for high current nets
  Larger clearances for sensitive, high voltage nets etc.
  Trace width depends on signal (I2C, SPI, UART)
  Trace width calculator tools (KiCad, online calculators)

## Slide 38: Design Rules Check (DRC) and note keeping
What is DRC
  Layout design vs. fabrication constraints (i.e. design rules)
  Checking critical parameters (min. trace widths, clearances, hole sizes etc.)
  Electrical rules (unrouted nets, short circuits etc.)
Run DRC often
  Personal learning
  To avoid extensive and laborious changes at later phases
Keep notes during layout design
  Traceability of design (steps, phases, details)
    What has been done, why and when?
    What has been changed, why and when?
  Personal learning (what has worked, what has not)
  Knowledge transfer

## Slide 39: PCB Layout tips, board
Board outline
  Try to keep the PCB dimensions small => lower costs, portable application, electrical performance
  If specific size for the PCB is needed, draw the PCB outlines first
  Choose edge cuts -> draw graphics with 0.01 mm or less width
Preferably use 2-layer board design (TOP and BOT copper layers).
Divide board layout to logical regions/ functional segments
  Power supply (high voltage/ high current regions)
  Analog circuits (sensors, LNAs, AD/ DA converters etc.)
    sensitive to switching noise
  Digital circuits (clock signals, CPUs, data buses etc.)
    Noisy
  Communication/ RF circuits
  Connectors

## Slide 40: PCB Layout tips, components
Place site critical components first
  Sensors (unobstructed sensing)
  Connectors (cable access)
  Display (visible)
  Buttons, SD card housing (accessible)
You may select SMD (Surface Mount Device) and through-hole (TH) components
  Enables viable assembly, modifying, repairing
  Only use package sizes you can work with
  SMD package size 0806, or larger, is recommend for passive components (resistors, capacitors)
Be aware of mechanical collisions and masking of components
  Build a mechanical proto from carton etc. for spatial verification

## Slide 41: PCB Layout tips, traces, cooling, test pads
Use short and wide traces to avoid EMI
Orthogonal routing, i.e. top layer for vertical tracks and bottom layer for horizontal tracks, or vice versa
Route traces manually, do not use auto-route
  Clean routing can help during debugging
Cooling
Take into account component power dissipation (P=UI)
  Component datasheets (section on cooling)
    Layout instructions (copper areas)
If heat sink is needed, leave enough room for it (linear regulator)
Add test pads/ “pins” for important and difficult to reach nets
  Ensure easy access to test pads/ pins

## Slide 42: PCB Layout tips, vias, bypassing, ground planes
Avoid vias
  Vias are common points of failure
  Avoid vias on signal traces/ fast nets
    Risk through hole related self-resonance disturbances to high frequency signals
Avoid placing vias in SMD pads (solder paste fleeing)
Avoid placing vias under component packages and leads (“legs”)
Place bypass capacitors as close as possible to IC power pins
Avoid ground loops (i.e. multiple return paths creating conductive loops)
  Fill unused board areas with continuous ground plane (copper pour)
  Use ground stitching vias around PCB edges (stable ground potential)
Use separate analog and digital ground planes in mixed signal systems (sensitive analog, noisy digital)
  Connect ground planes at a single low impedance point

## Slide 43: PCB Layout tips
Solder mask
  Useful in mass production manufacturing
    Improves manufacturability
    Protection against environment (corrosion etc.)
  But maybe not so much in prototyping…
    Testing, manual rework, modifications etc.
    Solder mask might need to be removed
Casing
  Casing design and layout design goes hand in hand
    Ensure mechanical compatibility
  Fixing PCB to casing (holes, screws etc.)
  Wall thickness (through-casing components/ structures)
    Displays
    Connectors etc.
  Vertical clearance of components (risk of collision with tall components)
  Placement of sensors (skin contact e.g.)

## Slide 44: Familiarize yourselves with the following layout design subjects
Division of components into functional segments
Traces
  Width and clearance based on net function (signal, ground, etc.)
Vias (based on net function)
  Number of vias
  Sizes (drill size, pad diameter, annular ring size)
  Ground stitching
Bypass capacitors
  Number of capacitors
  Capacitance values
  Placement
Copper planes in mixed signal systems
  separate analog and digital ground planes
And so on…

## Slide 45: Fabrication outputs

## Slide 46: Manufacturing files a.k.a. Gerber files
Data files for PCB manufacturing process (layers, traces, footprints, ground copper areas, vias, holes etc.)
Confirm that PCB Design Rule Check (DRC) shows no errors (none should appear!), check also the unconnected tab
Print the board as a 1:1 size print and verify that all the components fit ok (no collision, no masking, footprints match, etc.)
Generate at least the following manufacturing files
  TOP and BOT copper layers
  Edge cuts i.e. board outline
  Drill files
Manufacturing file format for copper layer and drill files
  Check manufacturer’s requirements
  Use Gerber (typically), absolute origin, unit as millimeters
Choose “do not tent vias” (tented i.e. via covered with solder mask)
  Untented vias may be useful later (debugging, fixing)
Check Gerber files with KiCad’s Gerber Viewer
  Layer alignment, no solder mask on soldering pads etc.

## Slide 47: PCB fabrication
PCB Design => physical implementation
PCB ordering:
PCBs are ordered from JLCPCB (Chinese manufacturer)
  Manufacturer’s online tool
    Upload your manufacturing files
    Files tested for manufacturability
    Cost estimation for PCB fabrication
Try to keep board manufacturing cost under 10 € / 5 pcs, or whatever is the minimum possible amount.
Requisite data files: TOP and BOT coppers, edge cuts and drill files
Fab Lab as PCB manufacturer
  PCB milling is available
  Via fabrication is limited (copper plating not available)
    Manual via finishing
    Designs with moderate number of vias might be conceivable

## Slide 48: Component placement on PCB

## Slide 49
Populating the board
Before soldering, visually inspect the PCB is free of faults
Check that only intended connections exist on PCB, i.e. there are no faulty short circuits (multimeter)
  Traces, planes, pads, vias
  Supply traces and ground
Clean PCB before soldering (cleaning solvent)
  SMD components
Assemble a single functional group at a time
  Start from power supply sections
  Test that implementation is functional before adding the next
Note component orientation (IC, pin 1)
Polarized components (anode, cathode)
  Electrolytic capacitors, transistors, diodes, LEDs etc.

## Slide 50: Populating the board
Manual soldering
  Facilities in Fab Lab (right?)
  New to manual soldering?
  => practice with some extra PCBs and components NOT with your scarce project resources
SMD components
  Manual paste dispensing and SMD pick and place manipulator for populating the board (Fab Lab?)
  Reflow soldering oven (Fab Lab)
  Guidance for the equipment is provided by the Fab Lab staff
Reflow soldering oven parameters
  Thermal profile matching with components and solder paste
    LF-MEDIUM profile; preheat 170deg C for 160 s, reflow 265 deg 120 s, cool to 90 deg

## Slide 51: Hardware testing

## Slide 52: Electrical testing
Visually inspect the PCB is free of soldering faults (reflow oven) and check conductivity of all the traces, vias, and pads with a multimeter
Check that only designed for connections exist on PCB
  Traces, planes, pads, vias
  Supply lines and ground
Powering up
  Use laboratory power supply
  Set current limit before powering up!
After powering up
  Observe and evaluate current consumption
  Check voltages at supply connectors, voltage regulators
  Supply voltages at components’ leads/ legs
Assembly and test a single functional part at a time, start from power supply sections (hand soldering)
Test that each part of the design/ implementation is functional before adding next one

## Slide 53: Casing

## Slide 54: 3D printing (optional)
There are many CAD software available for making 3D-models
Simple part design can be done, for example with FreeCAD
  https://www.freecad.org
  Basically, cut and combine blocks using Boolean operations between basic shapes to mold the simple shape you want (if not experienced, just try using cubes and cylinders)
  Remember to save often! (FreeCAD tends to be tricky with correction & undo functionality)
  Design your model so that usage of structural supports is minimized
    I.e. minimize the amount of overhangs with high slope angle
    Most basic 3D-printers can struggle with some complicated shapes
There exists plenty of other offline and online modeling CAD software, as long as the editor can output the model in STL-file format
For 3D printing:
The STL-file can be imported to the slicing software used to generate G-code (Geometric code) for the 3D-printer
Printers are available in Fab Lab, but in case of an emergency, we may be able to do printing in our robot laboratory printers.

## Slide 55: Project budget and HW ownership

## Slide 56: Project budget and HW ownership
Try to keep the price of your board as low as possible
  Preferably less than 80€, after that some negotiating will be necessary.
    Be very careful when choosing components that the chosen ones won’t be impacted by some supply chain issues.
If you pay all of the components yourself, you can keep the board after the course
  Otherwise, it needs to be returned to the assistant after the course
  Also, if you have bought some of the components, you can get them back after the course.
After the course, all hardware borrowed from university must be returned as well
  Programmers, develoment boards, etc.

## Slide 57
HW design support
Marko Kauppinen
marko.kauppinen@oulu.fi
Jaakko Huikari
jaakko.huikari@oulu.fi

## Slide 58
Discussion
Questions?
Comments?
Other?