## Slide 1: Embedded Systems Project (521423S) - Software

## Slide 2: Design phases
In practice:
Requirement specification, Technical specification, test plan, Schedule
Schematics, component ordering
Layout and manufacturing files, PCB ordering
Populating the board and electrical testing
Programming software and testing
Final demonstration and Final report

## Slide 3: Getting started
Absolutely make sure that there are no short / open circuits on your PCB.
First, only power on the essential hardware on your device, with a current limit set on your PSU (according to what you estimate your max. consumption is). If nothing smokes, it is a start at least.
Double and triple check that your JTAG / SWD, USB, or other programming interface, and UART connections to your system are correct.
  Some dev-kits may have schematics available, could be used as reference if you have MCU on your own custom board.
In some cases, your programmer might need to manipulate the reset wire
  For example, if accidentally some conflicting functionality affecting the programming pins is enabled, programmer may need to do things using the reset signal to recover programming access.

## Slide 4: Getting started, programming HW
Nucleo dev-kits with integrated ST-Link/V2 can be borrowed from us.
ESP32 dev-kits rely on internal JTAG of the MCU via USB data lines, or it can be programmed through USB-UART bridge
If your MCU is integrated to your board, a USB-UART converter, or other type of programmer may be required depending on the MCU.
Some dev-kits can be used to program external MCUs as well, if you have chosen to make your own fully custom board
  We have some Nucleo dev-kits that may be borrowed also for programming your own boards, with the ST-Link/V2 programmer integrated to those.
  ESP32 dev-kit could be used as a bridge for programming.
  We might also have a couple of old Atmel / Microchip ICE Basic kits available, but not guaranteed.
In other cases, you are pretty much on your own.

## Slide 5: Software design tips
Generally, use C or C++
  In this course, Assembly is very unlikely to be required, but typically it would be used for very critical computational / timing critical parts. However, compilers are pretty good at optimizing nowadays.
  Other languages are allowed, but may not be supported by us.
For documentation, create block diagrams of the main components and how they exchange information (i.e. data structures, algorithm interconnections, etc.)
Design the SW timing, like how many times a second something needs to be done
  Setup and handle the required interrupts (callback functions & data synchronization)
    If your dynamic variables are used in multiple locations of your code, synchronize when the new values are updated safely without chances of corruption.
  If you are polling data, take care of avoiding deadlocks and a waste of computing time.

## Slide 6: Software design tips
Read through the MCU datasheet and “cookbooks” for the parts you will be needing from the hardware
  For example: initializing timers and their counting modes, PWM generation, ADC/DAC, etc., and using their registers.
First tests are usually for seeing that connections and buses on the board are working
  Blinking LEDs, testing communications of I2C, SPI, UART,…
See how debug information can be read from the device
  For most ESP32 / STM32 dev-kits today, usually it is possible to at least “printf” stuff out in your terminal, over a virtual COM port if using USB for programming / debugging.
  In some cases, printing debug text out through the debug link may not be possible, so keep an additional UART port available on your device as an option…
Initially, plan and write simple testing routines for verifying that each software and hardware component is working correctly.

## Slide 7: Files and modules
Split software to modules, each module to its own file
  For example SPI.c, I2C.c, X_sensor.c, etc.
Name functions, variables, and parameters descriptively, like SPI_init(), SPI_transfer(uint8 *send_bytes, uint8 *receive_bytes), …
main.c should contain only high level function calls, and main state machine could be included in the main loop, if it is simple
While creating functions, briefly describe the operations implemented in the code sections with comments
  Try to document while you code, when you still remember what each part does…
  Anyone should be easily able to understand what at least your functions / methods do, based on your comments.
  There also exists some tools, like Doxygen, that may help documenting your code, at least to add standardized comments.
    Some IDEs provide ability to add standard comment blocks.
  At least try to keep the documentation blocks consistent, describing each parameter, return values, and functions.

## Slide 8: Some more general tips
Don’t write functions and algorithms that are very long and / or look obfuscated / hacky. The code should be easily reviewable.
Use structures and pointers in passing and handling groups of data instead of huge amounts of separate variables and values.
  Using pointers is generally more memory efficient; less memory and processor time is used when values do not need to be copied or replicated during calls.
    Can result in all sorts of issues if not done properly though.
    Probably in this work not the main concern, if not experienced in coding.
If weirdness is seen during debug, use volatile declarations to prevent compiler from optimizing certain pointers / variables
  Also, see how to setup the debug options in your chosen compiler and IDE, if needed.
  Outputting text & values through UART can help debugging in some cases, where the code might be optimized in a way that is otherwise difficult to follow in a debugger.

## Slide 9: Some more general tips
Code examples can be found from:
  Application notes / drivers from MCU / component manufacturer.
  Open-source libraries / functions.
  If you use STM32, some examples are included with the firmware libraries, more can be found on the internet.
  Mbed examples can be found, for example, from https://os.mbed.com/teams/ST/
Be aware that some of the development platforms & libraries;
  May result in a large firmware image for your device instead of including only the parts you need, especially in OS based platforms.
  May consume too much RAM on your device.
  May have parts that require certain clock speeds or specific types of MCU’s internal hardware blocks to be present for some functionalities.

## Slide 10: Getting started, Arduino
For beginners, we recommend using Arduino IDE, at least with the ESP32
First, find out if your chosen platform / MCU is supported in Arduino environment
For installing Arduino IDE
  https://www.arduino.cc/en/software
  Depending on your dev-kit or MCU, additional drivers may be required to enable communication through an UART-bridge chip, and / or through USB
Arduino development environment is also included as an option in some other programming IDEs
  Such as PlatformIO as a Visual Studio Code extension
    https://platformio.org
    At the time of checking, PlatformIO also included STM32Cube and Mbed environments. More of them later.

## Slide 11: Getting started, Arduino
If you choose to use Arduino IDE
  Choose your MCU / dev. board from Tools -> Boards. If it is not there, open boards manager and install relevant package containing your board / MCU.
    ESP32S3 Dev Module option should be compatible with the dev-kits that can be borrowed from us.
  For full debugging features via JTAG in ESP32 boards, access through USB-lines is required. In the ESP32-S3-DevkitC boards, the USB cable would be plugged to the “USB” port.
    USB mode has to be set to JTAG in Arduino configuration.
    “Virtual COM port” could be used to output text from your program to the Arduino IDE serial monitor simply by using the print commands within your software.

## Slide 12: Getting started, STM32Cube
Only relevant if using STM32 MCU based system
Using STM32Cube has less overhead, involves closer to hardware programming through STM32 HAL (Hardware Abstraction Layer) libraries, than using Operating System (OS) based implementations for STM32, like the Mbed OS
In general, you will need the STM32CubeMX package
  https://www.st.com/en/development-tools/stm32cubemx.html
  Should include the newest basic MCU firmware / HAL libraries
  But may need additional drivers & firmware from
    https://www.st.com/en/development-tools/stsw-link009.html
    https://www.st.com/en/development-tools/stsw-link007.html
Several IDE’s to choose from
  ST has the STM32CubeIDE environment (based on Eclipse)
    https://www.st.com/en/development-tools/stm32cubeide.html
    Nowadays, may also incorporate all of the functionality of STM32CubeMX, so it may not be needed separately
  Other extensions and plugins exist for VSCode, Eclipse, etc.

## Slide 13: Getting started, STM32Cube
Using STM32CubeMX GUI code generation tool
  Create a new project, choosing your board / MCU
  Configure all the required hardware blocks (clock inputs, GPIO pins, timers, ISP, I2C, etc. interfaces)
After the MCU setup, configure the code generation according to the toolchain / IDE you will be using
After generating the initialization code, the project can be imported to IDEs that supports STM32Cube
In the generated code, there are clearly marked sections for your own code, that will not change even if you change stuff using the STM32CubeMX GUI
  However, if you remove a peripheral or other block, you will lose the code within those generated functions, so be careful
    Preferably store your own code in libraries elsewhere, and use minimum amount of functions calls and algorithms in the generated code areas
    Backup often!

## Slide 14: Getting started, PlatformIO
If you are developing a “shield” type add-on board for your dev-kit, you may optionally use the PlatformIO IDE for VSCode (Visual Studio Code)
  Should be easy to install in VSCode, just install the PlatformIO IDE Extension
  Should already include everything for STM32Cube, Mbed, or Arduino environment development
  Note, PlatformIO might include older, sometimes buggy, libraries, so newer ones may have to be added manually depending on the dev-kit / MCU
    Sometimes may need to install the newer libraries and change the project specific configuration files to point at the correct location of the new libraries

## Slide 15: Getting started, Mbed
Mbed code is implemented for the Mbed OS, although using the full OS part is optional. Mbed abstracts away some of the hardware related details for somewhat simpler code.
Mbed code should be portable between platforms, and simple things can be implemented quickly and easily, but…
… seems to be somewhat of a hassle to setup own custom boards for Mbed, if it is not an already supported dev kit.
  Example of a complicated to setup your own custom board for Mbed, see: https://os.mbed.com/teams/ST/wiki/steps-to-create-a-new-STM32-platform
  Here are couple of examples of customizations required, if you make your own custom board with the same MCU as a corresponding Nucleo dev-kit
    https://os.mbed.com/users/hudakz/code/STM32F103C8T6_Hello/
    https://os.mbed.com/users/hudakz/code/MapleMini_Hello/
(Personally, have not used Mbed, but I heard it is simple to use with dev-kits and if Mbed “drivers” are available for your selected ICs)

## Slide 16: Debugging
At least on ESP32, there exists internal circuitry for JTAG (Joint Test Action Group), which is accessed via USB data lines
  To use more advanced debugging functionality on ESP32, use the USB port on the ESP32 to connect it to your computer
Other way to program and communicate with the ESP32, is to use the UART port.
  UART can also be used to get printed text from the code via print functions
    However, note that printing is typically not available if running a debug stub in your firmware that communicates with your debugger through the UART port. I.e. there is no “virtual COM port” available for printing text.
  To enable code upload via UART to ESP32, the boot pin has to be pulled to ground in power up (BOOT button).

## Slide 17: Debugging
Couple of Mbed and STM32Cube examples for outputting “printf” text via UART / “virtual COM port” with STM32 MCUs:
  https://os.mbed.com/docs/mbed-os/v6.8/debug-test/debugging-using-printf-statements.html
  http://www.emcu.eu/how-to-implement-printf-for-send-message-via-usb-on-stm32-nucleo-boards/

## Slide 18: Debugging, general tips
Regardless of which interface you use for programming, I would recommend to have at least one additional UART port available on your device as a back up plan, if it is otherwise difficult to get some text printed out from your code during debugging.
  Some tools / MCUs may not support running real-time debugging and printing text through the same UART port.
Your IDE should support placement of breakpoints, which you can use to halt the code at given points and check variables, if the required debug tools are installed and configured properly.
Set a break points in your code near, before, and after the problem point. Then step through the problem part of the code constantly checking on the related register and variable values.

## Slide 19: Debugging, general tips
Add break points / text prints in your code also into places where you suspect the code may jump to during misbehavior. For example, if you place a break point just before your main-function, you will see if the device resets at some point and the software execution starts from scratch, out of the main loop, when it is not supposed to.
  For example, when the MCU resets unexpectedly, like due to a supply voltage glitch or other problem.
If the MCU does not initialize and run properly, check the clock signals with oscilloscope and that the configuration is correct for the selected clock sources.
  Also check the reset signal, if it is pulled up or down correctly.

## Slide 20: Debugging, general tips
You can also measure your software timings outside the MCU by using some extra unused MCU pins by toggling them, and an oscilloscope / logic analyzer to check, for example:
  How long an interrupt loop lasts?
  How often it triggers?
    Spending too much time in interrupt routines or other loops may prevent other code from executing.
In communication problems, also check signals using an oscilloscope / analyzer
  Are the signal waveforms ok in signal lines (no excessive over- / undershoot, ringing, noise, amplitude issues etc.)?
  Does the line require a resistor to be added in series for smoothing the signal?
  Are the timing and frequencies correct?
  Is there a missing pull-up or pull-down resistor somewhere?
  Are the voltage levels okay for logic / measurement inputs?

## Slide 21: Final notes
Note that there are lots of real-time OS’s and programming tools for most MCUs
  If you are familiar with something else than what is in these slides, or you think is better, in general it is allowed to be used. Just discuss / specify your choice with the assistants first.
    There will be less support available for environments the assistants have not used before.
Everything borrowed must be returned after the course. Try not to modify the dev-kits themselves.
  Maybe some dev-kit jumper settings may have to be changed, but revert any changes after the dev-kit is no longer needed.
  If the dev-kit breaks or develops a fault, inform it to the assistants so a broken dev-kit won’t stay in circulation and cause headaches for students in the following years.

## Slide 22: Discussion